## Slide 1
STA platform offer 3 power modes :
    OFF / ON / Standby (STDBY)
  STDBY mode with no DDR powered. Platform current consumption estimation is around 35µA. Only PMU/RTC/AO_GPIO/BackupRAM/32KHz HW block powered. In this mode the boot flow is named “Cold Boot”
  We can add a sub-mode for which the DDR is still power-up during STDBY, STDBY-DDR. This mode is used when the SW Platform is moved in SuspendToRam (STR). In this mode DDR is moved in SelfRefresh and for DDR3L the consumption can be estimated around 20mA. In this mode the boot flow is the STR Boot
  In order to avoid the DDR consumption, a Mix-solution is the Suspend To Disk. Before to move in STDBY, the SW Platform reach the STR level and use the NVM memory to create snapshot images of DDR content. In this mode the boot flow is the STD Boot
STA Power Policies

## Slide 2
STA standard machine
  Cold Boot
  STR
  STD
STA Boot_m3os_from_m3xl
STA no u-boot
Index

## Slide 3
Cold Boot

## Slide 4
M3
Boot ROM
M3
XLoader
UBOOT
Linux Kernel
Device Tree
rootfs
M3
Sw
Cortex-A7
Secure
OP-TEE
SP-min
ATF BL32
User
Kernel
Pre-OS
Non Secure
Cortex-M3
Optional
Ensure secure boot
Legend
Loads from eMMC
Loads from eMMC & Calls
ATF BL2
OR
Calls
1
2
3.2
4
5
6
7
8
Cold Boot
SecureWorld
NonSecureWorld
M3 Xloader
M3 SW
BL2/BL32
Uboot
rootfs
Kernel/DTB
3.1

## Slide 5: Cold Boot Details
1. M3 XL authenticates and loads ATF BL2 from eMMC (raw paritition AP_XLOADER) to esram A7.
  M3 XL starts ATF BL2 (un-reset Cortex A7ss)
  M3 XL waits for pen
2. ATF BL2 loads M3 Sw from eMMC (FIP image) to esram M3
3.1 ATF BL2 releases pen 3.2 M3 XL jumps to M3 Sw
4. ATF BL2 loads Uboot from eMMC (FIP image) to DDR
5. ATF BL2 loads ATF BL32 from eMMC (FIP image) to esram A7 AFT BL2 jumps to ATF BL32
6. ATF BL32 jumps to uboot
7. Uboot loads Linux Image + Linux Device Tree from eMMC (bootfs image) to DDR
8. Uboot loads Linux Image from eMMC (bootfs image) to DDR
  Uboot jumps to Linux kernel
Esram
Memory DDR
Flash
Backup Ram

## Slide 6: STR Suspend sequence

## Slide 7: STR Suspend sequence
PMU
Block
Linux Kernel
rootfs
M3
Sw
Cortex-A7
Secure
BL32
User
Kernel
Non Secure
Cortex-M3
OP-TEE
OR
SP-MIN
Legend
SecureWorld
Call / Kick
NonSecureWorld
2.1
1
4
DDR storage
BL32
Snapshot
6
5
2.2
3

## Slide 8
1: Userland requests the STR to Kernel
2.1: Kernel freezes applications
Kernel suspends devices and saves theirs context
Kernel saves non secure eSRAM content in DDR
Kernel requests a stop of secondary CPU to ATF BL32
2.2: ATF BL32 puts secondary CPU in “Wait for Interrupt” state
  ATF BL32 requests a stop of secondary CPU to M3Sw
  M3Sw reset secondary CPU
3: Kernel requests the STR to ATF BL32
4: ATF BL32 Save Cortex-A7 secure context in ESRAM
ATF BL32 requests the STR to M3 OS
5: M3 OS produces the ATF BL32 snapshot in DDR
M3 OS writes a tag in Backup RAM to reference STR state
6: M3 OS requests the power off to PMU, the platform is moved in STDBY mode
STR suspend sequence details
Esram
Memory DDR
Backup Ram

## Slide 9: STR Resume sequence
M3
Boot ROM
M3
XLoader
Linux Kernel
(in suspend context)
rootfs
M3
Sw
Cortex-A7
Secure
BL32
(in supend context)
User
Kernel
Non Secure
Cortex-M3
Ensure secure boot
OP-TEE
OR
SP-MIN
Legend
Actions
Loads from DDR
Call / Kick
Loads from eMMC & Calls
Loads from eMMC
1.2
3
4
to A7 esram
M3 Xloader
1.1
2.2
2.1
rootfs
to M3 esram
ATFBL32
(suspend state)
M3 OS
(cold boot)
Linux Kernel

## Slide 10: STR Resume sequence
1.1 M3 XL detects STR resume thanks tag in Backup RAM M3 XL loads BL32 from DDR to esram A7
1.2 M3 XL un-reset the CPU A7ss ( call a7_start(…) ) M3 XL wait for the pen from BL32
2.1 ATF BL32 loads M3 OS from DDR to esram M3
2.2 ATF BL32 releases M3 XL pen
3 M3 XL jumps to M3 OS
4. ATF BL32 jumps to Linux Kernel
Esram
Memory DDR
Flash
Backup Ram

## Slide 11
M3
Boot ROM
M3
XLoader
UBOOT
Linux Kernel
Device Tree
rootfs
M3
Sw
Cortex-A7
Secure
OP-TEE
SP-min
ATF BL32
User
Kernel
Pre-OS
Non Secure
Cortex-M3
Optional
Ensure secure boot
Legend
Loads from eMMC
Loads from eMMC & Calls
ATF BL2
OR
Calls
1
2
3.2
4.1
5
6
7
8
4.2
fbios/sbios
Cold Boot for STD
SecureWorld
NonSecureWorld
M3 Xloader
M3 SW
Fbios/sbios
B1/BL2/BL32
Uboot
rootfs
Kernel/DTB
Quickboot
3.1

## Slide 12: Cold Boot for STD - Details
1: M3 XL authenticates and loads ATF BL2 from eMMC (raw partition AP_XLOADER) to esram A7.
  M3 XL starts ATF BL2 (un-reset Cortex A7ss)
  M3 XL waits for pen
2: ATF BL2 loads M3 OS from eMMC (FIP image) to esram M3
3.1: ATF BL2 releases pen 3.2: M3 XL jumps to M3 OS
4: ATF BL2 loads Uboot from eMMC (FIP image) to DDR ATF BL2 loads fbios/sbios from eMMC (FIP image) to DDR
5: ATF BL2 loads ATF BL32 from eMMC (FIP image) to esram A7 AFT BL2 jumps to ATF BL32
6: ATF BL32 jumps to uboot
7: Uboot loads Linux Device Tree from eMMC (bootfs image) to DDR
8: . Uboot loads Linux Image from eMMC (bootfs image) to DDR
  Uboot jumps to Linux kernel
Esram
Memory DDR
Flash
Backup Ram

## Slide 13: STD Suspend sequence
PMU
Block
Linux Kernel
rootfs
M3
Sw
Cortex-A7
Secure
BL32
User
Kernel
Non Secure
Cortex-M3
OP-TEE
OR
SP-MIN
Legend
SecureWorld
Call / Kick
NonSecureWorld
5.1
Falcon Module
fbios/sbios
2
1
3
4
Quickboot snapshot
6
eMMC storage
BL32
Snapshot
(including M3SW)
5.2
rootfs

## Slide 14
1: Userland requests the STD(hibernate) thanks to Quickboot procfs interface (/proc/falcon)
2: After linux Suspend preparation, snapshot module (falcon.ko) requests the next stage snapshot creation through fbios/sbios
3: fbios/sbios produces and stores the snapshot in a raw partition in eMMC
4: fbios/sbios request a SMC call (HIBERNATE) to Secure World ATF BL32.
  Beside the call itself the fbios entry point for resume is also notified.
5.1: ATF BL32 processes the usual STR procedure(move in suspend context) and sends an IPC message to M3 OS (HIBERNATE)
5.2 M3 Sw produces the ATF BL32 copy in DDR from A7 Esram , then produces a snaphot in a raw partition in eMMC
6: M3 Sw writes a tag in Backup RAM to reference STD state M3 Sw requests the power off to PMU, the platform is moved in STDBY mode (without DDR self-refresh procedure)
STD suspend sequence details
rootfs
Esram
Memory DDR
Flash
Backup Ram

## Slide 15: STD Resume sequence

## Slide 16: STD Resume sequence
M3
Boot ROM
M3
XLoader
Linux Kernel
(in suspend context)
rootfs
M3
Sw
Cortex-A7
Secure
BL32
(in supend context)
User
Kernel
Non Secure
Cortex-M3
Ensure secure boot
OP-TEE
OR
SP-MIN
Legend
Actions
Loads from DDR
Call / Kick
Loads from eMMC & Calls
Loads from eMMC
1
3
5.3
7
8
to A7 esram
fbios/sbios
Falcon
module
Quickboot snapshot
BL32
Snapshot
(including M3SW)
M3 Xloader
M3Sw
Fbios/sbios
4
5.1
9
6.2
ATF BL2
1.1
rootfs
ATFBL32 (suspend state)
2.2
2.1

## Slide 17
1: M3 XL detects STD resume thanks tag in Backup RAM
  M3xl forward this STD information in Shared data
  M3 XL authenticates and loads BL2 from eMMC to esram A7
  M3 XL unreset the CPU A7ss ( call a7_start(…) )
  M3 XL wait for the pen from BL2
2: BL2 authenticates and loads fbios/sbios binaries in dedicated DDR location from eMMC (FIP image)
  BL2 authenticates and loads M3sw in esram M3 and esram A7 from eMMC (FIP image)
3: BL2 knows thanks share data the resume is STD and not Cold Boot
  BL2 authenticates and loads ATF BL32 snaphot in dedicated DDR location from eMMC (raw partition ATTF SNAPSHOT)
4: Before to exit (wfi) BL2 releases the M3 XL pen
5.1: M3 XL reset CPU A7ss ( call a7_start(…) ) and shadow the ATF BL32 from DDR to esram A7
5.2: M3 XL unreset CPU A7ss ( call a7_start(…) ) and wait for the pen
6.1: ATF BL32 resume procedure is executed
6.2 :ATF BL32 releases the pen
7: M3 XL jump to M3 SW
8: ATF BL32 thanks to its context, knows the fbios entry point
ATF BL32 prepares the jump to NonSecure World with fbios entry point
9: fbios/sbios process the preload from quickboot snapshot
  fbios/ restore linux context (CPU/MMU) and jump to quickboot module
  kernel resume is processed
  Task thawing is done
STD resume sequence details
Esram
Memory DDR
Flash
Backup Ram

## Slide 18
Bootrom
M3
A7
ATF BL32
(in suspend state)
M3sw
M3xl
Linux kernel
(in suspend state)
Linux system - userland
Time
Mémoire NVM
DDR
M3xl
M3os
ATF BL2
Image ATF BL32 STD
Image Linux STD
Fbios/Sbios
ATF BL2
Fbios/Sbios
Image Flashed
Image built & Store at run-time
STD resume boot flow
M3 ESRAM
A7 ESRAM
0
1
2.1
2.2
3
5.1
9
8

## Slide 19
http://intranet.lme.st.com:8000/php-bin/opensdk_userguide/index.php/STA1XXX_-_A5/TC3/TC3P_-_SuspendToDisk_(STD)_based_on_QuickBoot_from_Ubiquitous#Architecture
STD references

## Slide 20
Cold Boot – machine m3os-from-m3xl

## Slide 21
Cold Boot – machine m3os-from-m3xl_no_uboot